## Slide 1
UCL ENGF0031 · SCENARIO 2 · LIVE DEMO
Cadence — Demo Run Card
Freeze-of-gait monitor · one ankle accelerometer · on-body OLED + wireless dashboard
RUN IT — in this order
1
Power both boards: CPX on its LiPo, ESP32 on a USB power bank. The CPX OLED shows the CADENCE splash.
2
On the laptop, join Wi-Fi Cadence-Hub (password cadence123), then open http://192.168.4.1/
3
Stand still and press button A on the CPX. "CALIB" shows for ~4 s, then the movement floor is set.
4
Walk normally → green LED ring + "WALKING" on the OLED + a live accel trace on the dashboard.
5
Provoke a freeze: buzz the foot fast in place — don't step → red ring + inverted "FREEZE", and freezes: N ticks up.
ON THE BODY (CPX)
OLED, big: WALKING / STILL / FREEZE
FI x.xx / 1.82 (ratio vs threshold)
E energy / floor (the movement gate)
freezes: N (confirmed-onset count)
LED ring: green = walk, teal = still
blue = calibrating, red = FREEZE
WIRELESS (ESP32)
Hotspot: Cadence-Hub
Password: cadence123
Open: http://192.168.4.1/
Dashboard: trace, freeze state, HR/SpO2
ESP32 LED: solid = browser on, blink = wait
Finger on the MAX30102 for HR/SpO2
IF IT MISBEHAVES
OLED blank — check SDA=A5 / SCL=A4 and a shared GND; some panels are at 0x3D, not 0x3C.
Dashboard won't load — be joined to Cadence-Hub (not your usual Wi-Fi); it has no internet, which is normal.
Stuck on STILL / never FREEZE — a clean stop reads STILL — buzz the foot fast in place; if still nothing, re-calibrate (button A while truly still).
FREEZE while standing still — re-calibrate; the movement floor is set too low for this wearer/surface.
HR / SpO2 blank — rest a fingertip on the MAX30102 and hold still ~10 s for a valid reading.
Research prototype — not a medical device. Detector: Freeze Index (Moore 2008) + movement gate (Bachlin 2010); the CNN is an offline benchmark.